## Slide 1: Autonomous Flag Finder
Burnout Squad
Jeremiah McCutcheon: Project Manager
David Koblah: Hardware Design
Michael Bates: Software Design

## Slide 2: System Description
This system is an autonomous robot designed to locate, identify and retrieve flags inside a room or maze.
It will utilize a camera and proximity sensors to navigate its environment.
The camera will wirelessly communicate with a computer in order to identify flags and retrieve them.
A microcontroller will control the movement of the tank, proximity sensors and servo motors to rotate the camera or retrieve the flags.
Jeremiah McCutcheon

## Slide 3: System Diagram
Jeremiah McCutcheon

## Slide 4: Tank mock-up
Jeremiah McCutcheon
Cover for PCB and other circuits

## Slide 5: Division of labor
Jeremiah: Bluetooth Serial Communication Interface with Mac, Video Camera Interface with Mac, Image Processing
David: BlueSMiRF receiving communication, Servo arm and Electromagnet interface, Flag Collection
Michael: Analog IR sensor implementation, Autonomous Navigation, MSP430 Code Interface, PCB, Budget
Jeremiah McCutcheon

## Slide 6: Tank Movement & Navigation

## Slide 7: Rover 5 Robot Platform
Michael Bates
Rover 5 Tracked Chassis [1]
2 Built-In DC Motors Allowing for Left Side and Right Side Control
Rugged White Plastic Body with Wire and Battery Compartment
Quick Connection wires for H-Bridge
Used in Previous Projects

## Slide 8: H-Bridge
ST Microelectronics: Dual Full Bridge Driver [2]
Controls 2 Motors:
  EnA=Left Track
  EnB=Right Track
Controls 2 Directions for Each Motor:
  In1=Left Forward
  In2=Left Reverse
  In3=Right Forward
  In4=Right Reverse
Michael Bates

## Slide 9: MSP430G2553
MSP430G2553 Launchpad [3]
Low Cost ($15)
UART Capability
SPI Capability
Removable IC
On Board Programming
9600 Baud Rate
Multiple Timer-A Interrupt Registers
Sufficient Pins
Michael Bates

## Slide 10: IR
Pololu IR Sensor [4]
Can Operate on 5V
Distance Measuring Range: 4”-32”
Only Uses 1 Signal Wire
Uses an Analog Signal That Can Be Easily Converted to Digital for Easy to Use Values for Navigation
Michael Bates

## Slide 11: Flow Chart
Michael Bates
5 Primary Movements
  Forward
  Veer Left
  Veer Right
  Left
  Right
Use Timer-A for Movement Duty Cycle
  Timer-A0 Controls Left Side
  Timer-A1 Controls Right Side
  Allows for Veering Movement

## Slide 12: Test Video
Michael Bates

## Slide 13: Macbook Interface

## Slide 14: Macbook Application
Jeremiah McCutcheon

## Slide 15: Bluetooth BlueSMiRF
9600 Baud
Controls rover in manual mode and during blob detection
Jeremiah McCutcheon
SparkFun [5]

## Slide 16: WiFi Camera
App downloads images from the IP camera
Images are analysed by OpenCV
Camera Mount
Jeremiah McCutcheon
Amazon: Magendara WiFi Camera [6]

## Slide 17: SDL: Simple DirectMedia Layer
Made for game creation
Renders GUI elements
Incomplete GUI
Jeremiah McCutcheon

## Slide 18: Keystroke Movement Control
Reads the state of the keyboard
Sends Bluetooth commands for keys pressed
Jeremiah McCutcheon
SDL Wiki: Keystate [7]

## Slide 19: OpenCV Blob Detection
The image is masked for green
The program reads the blob size and location
Movement commands are sent via bluetooth
The flag is retrieved when in range
Jeremiah McCutcheon

## Slide 20: Flag design
Jeremiah McCutcheon

## Slide 21: Flag Seeker Videos

## Slide 22: Flag Retrieval

## Slide 23: Servo Arm Components
Voltage Range: 4.8V-6.0V Voltage Range: 4.8V-6.0V
Max. Current Drain: 285mA Max. Current Drain: 180mA
Max . PWM Range: 600-2400µs Max . PWM Range: 1000-2000µs
HS-785HB
HS-422
David Koblah
Servo City [8]

## Slide 24: Electromagnet
Requires signal to activate magnet. Only activated when required for flags
Working Voltage : 5V Standby Current: 200µA
Working Current: 400mA Load Weight: 1kg
David Koblah
Mouser.com [9]

## Slide 25: Completed Rover (“Under The Hood”)
David Koblah
Maximum Length (Arm at Full Length:
402 mm
Maximum Width:
225 mm

## Slide 26: Robot Arm Sequence
David Koblah

## Slide 27: Weight of Robot
Main components:
Robot Arm (201g) + 2 2000mAh Batteries (70g)+
Rover Chassis (1179.34g) + Camera (22.68g) +
Circuit components, Wiring, Sensors & Miscellaneous (50g)
Estimated Total Weight= 1523.02g = 3.357lb
David Koblah

## Slide 28: Power Estimates
Power Sources Available:
9.6V, 2000mAh Battery x2 : 2 x (2A x 9.6V) = 38.4W
Battery Pack for Robot Arm: 5V x 2.4A = 12W
Inbuilt Camera Lithium Polymer Battery: 3.7V x 0.48A = 1.78W
Total Power Available = 52.18W
Estimated Power Consumed = Motors (12.96W) + Camera(1.78W) + Robot Arm(4.325W) + PCB & Sensors(6W) = 25W
Ideal Runtime of Rover With Load =2000mAh/1800mA= 67 mins
David Koblah

## Slide 29: Safety Concerns
Our primary safety concerns dealt with managing the 9.6V battery to avoid any fires and over volting microcontroller circuits.
Making sure not to connect to TTU with lab router. Because our devices would violate security protocols.
Wearing appropriate Personal Protective Equipment
  Pants
  Closed Toed Shoes
  Safety Glasses
Making sure to perform all painting OFF campus.
David Koblah

## Slide 30: Gantt Chart
Jeremiah McCutcheon

## Slide 31: Budget
Michael Bates

## Slide 32: Budget Continued
Michael Bates

## Slide 33: Final Parts List
Michael Bates

## Slide 34: Mass Production (1000) Cost
Michael Bates
Sell each for $425.38 to make 50% profit ($425,382.57).

## Slide 35: References
[1] Sparkfun Rover 5 Robot Platform, https://www.sparkfun.com/products/10336
[2] ST Microelectronics H-Bridge dual motor controller : http://www.st.com/en/motor-drivers/l298.html
[3] Texas Instruments User’s Guide, MSP430G2553 Launchpad Development Kit, http://www.ti.com/tool/MSP-EXP430G2
[4] Pololu, Sharp GP2Y0A21YK0F Analog Distance Sensor 10-80cm, https://www.pololu.com/product/136
[5] SparkFun BlueSMiRF Silver: https://cdn.sparkfun.com/datasheets/Wireless/Bluetooth/Bluetooth-RN-42-DS.pdf
Michael Bates

## Slide 36: References Continued
[6] Amazon- https://www.amazon.com/Tenergy-Standard-Connector-Security-Rechargeable/dp/B001BA292A
[7] SDL wiki: SDL keystate: https://wiki.libsdl.org/SDL_GetKeyboardState
[8]Mouser.com https://www.mouser.com/ds/2/744/Seeed_101020073-1217554.pdf
[9] Servo City https://www.servocity.com/
Michael Bates

## Slide 37: Questions?