## Slide 1: Autonomous Flag Finder
Burnout Squad
Jeremiah McCutcheon: Project Manager
David Koblah: Hardware Design
Michael Bates: Software Design

## Slide 2: System Description
This system is an autonomous robot designed to locate, identify and retrieve flags inside a room or maze.
It will utilize a camera and proximity sensors to navigate its environment.
The camera will wirelessly communicate with a computer in order to identify flags and retrieve them.
A microcontroller will control the movement of the tank, proximity sensors and servo motors to rotate the camera or retrieve the flags.
David Koblah

## Slide 3: System Diagram
Jeremiah McCutcheon

## Slide 4: Division of labor
Jeremiah: Bluetooth Serial Communication Interface with Mac, Video Camera Interface with Mac, Image Processing
David: BlueSMiRF receiving communication, Servo arm and Electromagnet interface, Flag Collection
Michael: Analog IR sensor implementation, Autonomous Navigation, MSP430 Code Interface, PCB, Budget
Jeremiah McCutcheon

## Slide 5: Safety Concerns
Our primary safety concern this week has been managing the 9.6V battery to avoid any fires and over volting microcontroller circuits. We may also add a warning signal to our design to prevent fellow lab users from running into the rover.
Making sure not to connect to TTU with lab router.
Wearing appropriate Personal Protective Equipment
  Pants
  Closed Toed Shoes
  Safety Glasses
Making sure to perform all painting OFF campus.
David Koblah

## Slide 6: Last Week’s Deliverables
Jeremiah
Complete Blob Detection✅
Write ‘Blob Mode’ Code✅
RSSI with all 4 Blue SMiRF’s✅
Michael & David
Interface Servo Arm and Electromagnet Code with Sensor Navigation Code ✅
Run Tests with Sensor Movement and Servo Arm ❌
Finalize power distribution for the entire system ✅
Jeremiah McCutcheon

## Slide 7: Robot Arm Slave Code Using SPI
David Koblah

## Slide 8: Power Solution For Flag Finder System
David Koblah
Will power Rover and Printed Circuit Board
Will power Bluetooth modules on Flags
9.6V 2000mAh Pack [1]
Coin Battery Holder [2]

## Slide 9: Power Solution For Flag Finder System
David Koblah
Adafruit [3]
Will power Servo Arm Board

## Slide 10: Serial Peripheral Interface (SPI)
Michael Bates

## Slide 11: Motor Stop Servo Go Code
Michael Bates
Disable left and right motors for 8 seconds while servo arm collects flag

## Slide 12: SPI Test Video and Navigation Test Video
Michael Bates

## Slide 13: Blob Detection
Jeremiah McCutcheon
Blob Parameters [4]
Create new blob detector object & KeyPoint vector
Establish cv namespace &
Create parameter data structure
Blob Parameters

## Slide 14: Blob Detection
Jeremiah McCutcheon
inRange function opencv [5]
Isolate Green
Run blob detection

## Slide 15: Blob Detection
Jeremiah McCutcheon
Original
Green Isolated

## Slide 16: ‘Blob Mode’
Jeremiah McCutcheon
inRange function opencv [5]
Blob location on image

## Slide 17: RSSI
Jeremiah McCutcheon

## Slide 18: Gantt Chart
Jeremiah McCutcheon

## Slide 19: Budget
Michael Bates

## Slide 20: Budget Continued
Michael Bates

## Slide 21: Next Week’s Deliverables
Jeremiah
Flag Retrieval tests
Figure out what to do with RSSI?
Assist with hardware and construction
Michael & David
Run Tests with Sensor Movement and Servo Arm
Construction and wire management
Complete replica PCB design using Solderable Breadboard (David)
David Koblah

## Slide 22: References
[1] Robotpark- http://www.robotpark.com/2x2032-Coin-Cell-Battery-Holder-6V-output-with-On-Off-switch
[2] Amazon- https://www.amazon.com/Tenergy-Standard-Connector-Security-Rechargeable/dp/B001BA292A
[3] Adafruit, USB Micro-B Breakout Board, https://www.adafruit.com/product/1833?gclid=CjwKCAjw2dvWBRBvEiwADllhnzXv3tp1a9778W7LGTnBvy1PneBgkcm03iFKNXeWRFJ7it8sTilNjhoCUDsQAvD_BwE
[4] Blob parameters opencv: https://www.learnopencv.com/blob-detection-using-opencv-python-c/
[5] InRange function opencv: https://stackoverflow.com/questions/38082004/opencv-inrange-function
Michael Bates

## Slide 23: Questions?